## Slide 1: MODBUS
OpenAT implementation

## Slide 2: MODBUS over serial : openAT implementation
Asynchronous (callback driven), multi-instance and task safe (can be initialized in several task contexts)
MODBUS_InitContext to initialize the stack
  Set the line parameters (mainly, parity, baudrate, timeout) and the modbus mode (RTU or ASCII).
  Register a callback to receive MODBUS responses
MODBUS_ReleaseContext to close the stack
Enable/disable a GPIO pin to signal Rx/Tx phases
  MODBUS_EnableHardwareSwitch
  MODBUS_DisableHardwareSwitch

## Slide 3: MODBUS over serial : openAT implementation
Memory footprint
  RTU: <2Kb in heap, ASCII: <5Kb in heap
8 main MODBUS functions
  MODBUS_ReadCoils
  MODBUS_ReadDiscreteInputs
  MODBUS_ReadHoldingRegisters
  MODBUS_ReadInputRegisters
  MODBUS_WriteSingleCoil
  MODBUS_WriteSingleRegister
  MODBUS_WriteMultipleCoils
  MODBUS_WriteMultipleRegisters

## Slide 4: MODBUS over serial
OpenAT implementation main specifications
  Asynchronous, task safe, low memory footprint
    Rely on open UART interface: end of transmission is detected by a blank ranging from 3.5 to 4.5 characters time in compliance with MODBUS specs.
  Enable harware switch on any elligible GPIO
  8 main modbus functions in RTU or ASCII mode
    Read coils
    Write single/multiple coils
    Read holding register
    Write single/multiple registers
    Read discrete inputs
    Read input registers
  Performances: read 10 holding registers starting at 0x0000
    9600 bauds =>1048 requests in 60 seconds
    19200 bauds =>1785 requests in 60 seconds
  Available Lua implementation on OpenAT