## Slide 1: Monitoring Simple DB tools how to

## Slide 2: Simple DB tools: SDB
SimpleDB
    sdb = require “simpledb”
    db = sdb:newsdb(columns, maxnbofentries)
      Create an instance of a Simple DB, columns is a table containing the name for each columns, maxnbofentries is the maximum number of entries that the table will hold. If more entries are added, older ones will be discarded
    db:addrecord(…)
      Add one record (a row) into the Simple DB object
    db:clean()
      Clean the Simple DB object (remove all the data)
    db:data()
      Return a data table that can be directly used in one of the sendXXX functions to send the data to the Server.

## Slide 3: Simple DB tools: RRD (1)
Round-Robin DB (1)
    sdb = require “simpledb”
    db = sdb:newsdb(columns, maxshortterm, maxlongterm)
      Create an instance of an RRDB, columns is a table containing the name for each columns, maxshortterm is the maximum number of short term entries, and maxlongterm is the maximum number of long term entries.
      The column table also holds consolidation method that will be used to build long term entries.
    db:addrecord(…)
      Add one record (a row) into the short term entries of this RRD object

## Slide 4: Simple DB tools: RRD (2)
Round-Robin DB (2)
    db:clean()
      Clean the RRD object (remove all short and long term data)
    db:data()
        Return two data tables, one for short and the other for long term entries.
Internally it uses two simple DB: one for short term entries and the other one for long term entries

## Slide 5: Simple DB tools: RRD (3)
A consolidation of the data is done each time the number of short term entries is reaching the maxshortterm value.
The consolidated data (=one record) is then stored into the long term table.
Consolidation methods can be one of:
    last(default), first, min, max, mean, median, middle, modal,
    A number referencing a column so that it will take the corresponding value

## Slide 6: Examples
Sends an event when the system temperature reach a fixed value
Store signal and battery values in a historical database that contains short and long term (consolidated) samples.
Sends the long term content of the database on each Server connection, and both long -- and short term data on overheating event
Local sdb = require “simpledb”
local db = sdb:newrrd({"timestamp", "battery", "signal"}, 6, 12)
local periodictrigger = onperiod(10*60) – trig every 10 minutes
local aquireaction = function()
db:addrecord(time(), system.batterylevel, system.cellularrssi)
end
connect(periodictrigger, aquireaction)
local overheatingtest = function() return system.temperature > 55 end
local overheatingtrigger = filter(overheatingtest, onchange("system.temperature"))
local overheatingaction = function()
local event = {timestamp = time(), code = 102, data = system.temperature}
sendevents("monitoring", event)
local shortterm, longterm = db:data()
sendcorrelateddata("monitoring", shortterm)
sendcorrelateddata("monitoring", longterm)
db:clean()
connecttoserver()
end
connect(overheatingtrigger, overheatingaction)
local connectaction = function()
local shortterm, longterm = db:data()
sendcorrelateddata("monitoring", longterm)
db:clean()
end
connect(onconnect(), connectaction)

## Slide 7: Examples
Monitor the signal level, every 30 minutes
Every day at midnight send the minimum value of the signal, and the date when it happened
-- Create a db with 2 columns,
-- the consolidation for col2 is taking the min value,
-- the consolidation for col1 is taking the value on the same row as the one taken on col2
local sdb = require “simpledb”
local db = sdb:newsdb({"timestamp", "signal", timestamp = 2, signal = "min"}, 48)
local periodictrigger = onperiod(30*60) -- every 30 minutes
local aquireaction = function()
db:addrecord(time(), system.cellularrssi)
end
connect(periodictrigger, aquireaction)
local midnighttrigger = ondate("0 0 * * *") -- CRON: every day at 0:00
local midnightaction = function()
sendcorrelateddata("monitoring", db:consolidate())
db:clean()
connecttoserver(10)
end
connect(midnighttrigger, midnightaction)