## Slide 1: How to use GPIO module into Monitoring

## Slide 2: GPIO module: Digital inputs
Digital inputs
    gpio = require “gpio”
      Load monitoring module
    inputpoller = gpio.newDigitalInputs(tab, configtable, pollingperiod)
      Create an instance of a GPIO input poller. Stored values of configured pins into table tab. Configured pins will be read every pollingperiod ms.
    configtable is a list of digital inputs with an associated name:
      { {name =‘i0’, pin = 7} , {name =‘i1’, pin = 10}, …}
    inputpoller:release()
      Release inputpoller instance. Configured pins will be not polled anymore.
    An input can not be subscribed two times !

## Slide 3: GPIO module: Digital outputs
Digital outputs
    gpio = require “gpio”
      Load monitoring module
    outputswriter = gpio.newDigitalOutputs({ {name = ‘O1’, pin = 7}, …})
      Create an instance of a GPIO input poller. Stored values of configured pins into table tab. Configured pins will be read every 100ms.
    outputswriter:write(“ouputname”, value)
      Write value into the output with the given name.
    outputswriter:release()
      Release outputswriter instance. Configured pins can not be wrote anymore.
    An output can not be subscribed two times !

## Slide 4: GPIO module: Analog inputs (1)
Analog inputs
    gpio = require “gpio”
    analoginputs = gpio.newAnalogInputs(tab, configtable, pollingperiod)
      Create an instance of an analog input poller.
      Stored read values of configured analogs into table tab.
      Analogs will be read every pollingperiod/nb_analogs ms.
    configtable is a list of digital inputs with an associated name and some specifcs configuration:
    { {name =‘name’, id = analogId, deadband = x, scalefactor = x, offset = x}, …}
      deadband is a range of values in which analog input will be not updated.
      scalefactor is multiplicator factor divided by 65536
      offset is a positive or negative value to be added to the result of read value mutilplied by the scalefactor.

## Slide 5: GPIO module: Analog inputs (2)
    analoginputs:release()
      Release analoginputs instance.
    Only one instance of an AnalogInputs can be create.

## Slide 6: Examples
Sends an event when value of input I0 change
Write to output O1 the value of input I1
-- Create a gpiopoller for pin 10 and 8 and create an output writer for pin 10
local gpio = require "gpio“
local poller,err = gpio.newDigitalInputs(system,{{name='I0', pin=10}, {name='I1', pin=8},100)
local writer,err = gpio.newDigitalOutputs({{name='O1', pin=10}})
local function eventaction()
sendevents('monitoring',{{timestamp = time(), code = 102, data = "I0 value " .. system.I0}});
connecttoserver()
end
local function writeaction()
writer:write("O1", system.I1)
end
connect(onchange("system.I0", eventaction)
connect(onchange("system.I1", writeaction)

## Slide 7: Examples
Sends an event when the temperature reached 25°
Use input I0 and I1 as an input port P0.
Send a data for each new value of port P0
local gpio = require "gpio"
local poller,err = gpio.newDigitalInputs(system,{{name='I0', pin=10}, {name='I1', pin=8}},100)
local analogInputs,err = gpio.newAnalogInputs(system,{{name='temperature', id=2}},100)
local function temperatureaction()
sendevents('monitoring',{{timestamp = time(), code = 102, data = system.temperature}});
connecttoserver()
end
local function portaction()
local value = gpio.toIntValue({system.I0, system.I1})
local data = { P0 = {timestamps = {time()}, data ={value}}};
sendtimestampeddata('P0',data);
connecttoserver()
end
connect(onthreshold(25,"system.temperature","up"), temperatureaction)
connect(onchange("system.I0","system.I1"), portaction)